## Slide 1: Bandwidth measurement & analysis
EE533 Reading#2
Haoran Fan
USC ID: 9122-3344-95

## Slide 2: 1. Introduction
Tools:
  Platform: PlanetLab
  Tools: pathrate
Goals:
  Find bandwidth characteristics of network path
  Insights into potential trends of bandwidth for estimation

## Slide 3: 2. Measurement Analysis
Set 1:
  Date: Aug 11th 2004 ~ Sep 6th 2004
  PlanetLab Version: Version 2
  Return Data: High Capacity Estimate
Set 2:
  Date: Jan 5th 2005 ~ Jan 18th 2005
  PlanetLab Version: Version 3
  Return Data: High Capacity Estimate

## Slide 4: 2. Analysis - Overview
 | Set 1 | Set 2
# of Nodes | 279 | 178
# of pairs | 12006 | 21861
Min Capacity | 0.1 Mbps | 0.3 Mbps
Max Capacity | 1210.1 Mbps | 682.9 Mbps
Avg Capacity | 63.44 Mbps | 64,03 Mbps
Medium Capacity | 24.5 Mbps | 91.4 Mbps
Standard deviation | 119.22 Mbps | 43.78 Mbps
Difference may because of…
  PlanetLab Version updated to v3
  Infrastructure updated
  Tools error

## Slide 5: 2. Analysis - Overview
 | Set 1 | Set 2
# of Nodes | 279 | 178
# of pairs | 12006 | 21861
Min Capacity | 0.1 Mbps | 0.3 Mbps
Max Capacity | 1210.1 Mbps | 682.9 Mbps
Avg Capacity | 63.44 Mbps | 64,03 Mbps
Medium Capacity | 24.5 Mbps | 91.4 Mbps
Standard deviation | 119.22 Mbps | 43.78 Mbps
Observation
  Prefiltering of set 2 data nodes: extremely high/low nodes in set 1 are relatively unstable
  Limited the number of nodes per site to 2 in Set 2

## Slide 6: 2. Analysis - Distribution
Observation
  Set 1: most under 50 Mbps
  Set 2: most between 80 ~ 120 Mbps
Capacity (Mbps) | Set 1 |  | Set 2 | 
 | # of pairs | % | # of pairs | %
C < 20 | 4013 | 33.42 | 6733 | 30.8
20 < C < 50 | 4246 | 35.37 | 1910 | 8.74
50 < C < 80 | 674 | 5.61 | 1303 | 5.96
80 < C < 120 | 2193 | 18.27 | 11744 | 53.92
120 < C < 200 | 207 | 1.72 | 139 | 0.64
200 < C < 500 | 392 | 3.27 | 21 | 0.096
C > 500 | 281 | 2.34 | 11 | 0.05

## Slide 7: 2. Analysis – Asymmetry Factor
Meaning:
  Test the bandwidth in bi-direction
  If factor -> 0, it means that this path’s bandwidth is more symmetry for both direction
Formular

## Slide 8: 2. Analysis – Asymmetry Factor
Asymmetry Factor | Set 1 |  | Set 2 | 
 | # of pairs | % | # of pairs | %
a < 0101 | 132 | 6.08 | 1943 | 21.49
0.01 < a < 0.05 | 395 | 18.19 | 3237 | 37.74
0.05 < a < 0.1 | 165 | 7.6 | 817 | 9.52
0.1 < a < 0.2 | 243 | 11.19 | 880 | 10.26
0.2 < a < 0.5 | 328 | 15.1 | 1111 | 12.95
0.5 < a | 909 | 41.85 | 870 | 10.14
Observation
  Nodes in Set 2 is much more symmetry than Set 1
Possible Reason
  PlanetLab Software version upgraded
  Pathrate version
Question:
  Can we say it infers that the infrastructure changes?

## Slide 9: 2. Analysis – Common Nodes
Observation
  Biggest Change: From 20 ~ 50 Mbps to 80 ~ 120 Mbps
Capacity (Mbps) | Set 1 |  | Set 2 | 
 | # of pairs | % | # of pairs | %
C < 20 | 1041 | 30.54 | 909 | 26.66
20 < C < 50 | 1491 | 43.74 | 103 | 3.02
50 < C < 80 | 105 | 3.08 | 180 | 5.28
80 < C < 120 | 587 | 17.22 | 2205 | 64.68
120 < C < 200 | 37 | 1.09 | 12 | 0.35
200 < C < 500 | 86 | 2.52 | 0 | 0
C > 500 | 62 | 1.82 | 0 | 0

## Slide 10: 2. Analysis – Common Nodes Factor
Observation
  Significant reduced asymmetry factor for Set 2
Asymmetry Factor | Set 1 |  | Set 2 | 
 | # of pairs | % | # of pairs | %
a < 0101 | 65 | 9.83 | 145 | 21.94
0.01 < a < 0.05 | 167 | 25.26 | 299 | 45.23
0.05 < a < 0.1 | 57 | 8.62 | 86 | 13.01
0.1 < a < 0.2 | 64 | 9.68 | 70 | 10.59
0.2 < a < 0.5 | 83 | 12.56 | 48 | 7.26
0.5 < a | 225 | 34.04 | 13 | 1.97

## Slide 11: 2. Analysis - Correlation Study
Goals
  Find if there is possible correlation between latency and bandwidth
Method
  Find closest nodes – shortest latency
  Find max bandwidth
  Ratio of max bandwidth to bandwidth to shortest latency node’s bandwidth
    If closer to 1, means the correlation between bandwidth and latency is stronger

## Slide 12: 2. Analysis - Correlation Study
Observation
  Did not find such correlation
Conclusion
  Might have more degree of rank-order correlation

## Slide 13: 3. Summary & Conclusion
Present data:
  Large scale measurement
  end-to-end capacity of path between PlanetLab nodes
Tools
  PlanetLab
  Pathrate
Conclusion
  Capacity of Path
    An order of magnitude difference
  Capacity Symmetry is not necessary
  Bandwidth limited implemented
  Correlation between latency and bandwidth should be investigate in the future

## Slide 14: Thanks for watching
EE533 Reading#2
Haoran Fan
USC ID: 9122-3344-95