## Slide 1: Avoiding ISA Bloat with Macro-Op Fusion for RISC-V
EE533 Reading#4
Haoran Fan
USC ID: 9122-3344-95

## Slide 2: 1. Introduction
CISC processors
  e.g., x86
  micro-ops to decompose complex instructions
Traditional RISC architectures aim
  simplicity, efficiency, and scalability
RISC-V
  minimalistic, free, and open ISA designed for a range of implementations

## Slide 3: 2. Motivation
Many modern ISAs suffer from:
  instruction set bloat
  adding complexity
  cost
RISC-V seeks to maintain a clean and efficient ISA
Macro-op fusion can reduce:
  effective instruction counts without increasing ISA complexity
evaluates RISC-V's performance compared to
  x86-64, IA-32, ARMv7, and ARMv8

## Slide 4: 3. Methodology
Benchmark Suite:
  SPEC CINT2006 for performance evaluation
ISAs Compared:
  ARMv7, ARMv8, IA-32, x86-64, RISC-V (RV64G, RV64GC)
Metrics:
  Dynamic instruction count, instruction bytes fetched, effective instruction count
Tools:
  GCC 5.3 compiler, perf utility, QEMU simulator for ARMv8

## Slide 5: 4. Key Results - Instruction Counts
RV64G
  executes 16% more instructions than x86-64
  within 2% of x86-64's retired micro-op count
RV64GC (compressed variant)
  improves code density
  Macro-op fusion reduces RISC-V's effective instruction count by 5.4%

## Slide 6: 4. Key Results - Instruction Density
x86-64
  fetches 3.71 bytes per instruction on average
RV64G
  fetches 23% more instruction bytes per program than x86-64
RV64GC
  fetches 8% fewer instruction bytes than x86-64, making it the densest ISA

## Slide 7: 5. Macro-Op Fusion Mechanism
Definition:
  Combining common multi-instruction idioms into a single operation
Examples:
  Compare-and-branch sequences fused into one instruction
  Indexed loads and arithmetic sequences fused for efficiency
  Clear upper word operations optimized via fusion

## Slide 8: 6. Design Recommendations
For Compiler Writers:
  Optimize instruction scheduling for macro-op fusion.
  Improve register allocation to enable fusion-friendly code.
For Hardware Designers:
  Implement fusion-friendly decode units in high-performance RISC-V cores
  Optimize instruction fetch to support fusion in single-issue cores

## Slide 9: 7. Key Takeaways
RISC-V can match or exceed CISC performance with effective microarchitectural techniques
Macro-op fusion allows RISC-V to maintain simplicity while achieving high efficiency
Combining macro-op fusion with compressed instruction sets results in superior code density
No need to expand ISA complexity—fusion achieves the benefits of richer ISAs without bloat

## Slide 10: 8. Conclusion & Future Work
Conclusion:
  RISC-V achieves competitive performance using macro-op fusion without ISA bloat
Future Work:
  Extend analysis to floating-point and JIT workloads
  Investigate further compiler optimizations for better fusion opportunities
Final Thought:
  RISC-V remains an elegant and scalable ISA, benefiting from modern microarchitectural techniques

## Slide 11: Thanks for watching
EE533 Reading#4
Haoran Fan
USC ID: 9122-3344-95