## Slide 1: NetFPGA: A Tool for Network Research and Education
EE533 Reading#5
Haoran Fan
USC ID: 9122-3344-95

## Slide 2: 1. Introduction
Key Problem:
  Traditional network education lacks hands-on experience at lower network layers (Link & Physical)
Objective:
  Provide students and researchers with a platform to build real networking hardware
Solution:
  NetFPGA, an open, easy-to-use hardware platform for learning, experimentation, and research

## Slide 3: 2. NetFPGA Version 1
Developed:
  2001
  first used in 2003
Features:
  Three Altera EP20K400 APEX FPGAs.
  8-port Ethernet controller (10 Mbps).
  No on-board CPU (Software runs on external machines).
  Remote access for debugging & learning.

## Slide 4: 2. NetFPGA Version 1
Classroom Use: “Build Your Own IP Router”
  Students design and implement an IPv4 router
  Implements a fast path in hardware, slow path in software
Key Learning Outcomes:
  Understanding of hardware-software trade-offs in networking
  Exposure to networking protocols (OSPF, ARP, NAT, etc.)
Limitations
  Non-standard format (custom rack & backplane).
  Limited speed (10 Mbps).
  No on-board CPU (limited software performance).
  Limited OS support (mainly Linux/Solaris).

## Slide 5: 3. NetFPGA Version 2
Developed:
  2004,
  first prototypes in 2005.
Key Upgrades:
  Standard PCI format (easier integration with PCs).
  4 x 1Gbps Ethernet ports (higher performance).
  Xilinx Virtex-II Pro FPGA (supports embedded CPUs).
  Improved development tools (supports Windows & Linux).
  Hands-on access possible (students work directly with boards).

## Slide 6: 3. NetFPGA Version 2
New Classroom Configuration
  Lab setup:
    1 control board per PC.
    4 student boards connected for independent projects.
  Hardware Simulation & Debugging:
    Uses industry tools like VCS, ModelSim, and Xilinx ISE.
    Supports packet capture via pcap for debugging.

## Slide 7: 4. Research Applications
Beyond the classroom:
  NetFPGA-v2 enables high-speed networking research.
Key Research Projects:
  1. Rate Control Protocol (RCP) – TCP optimization research at Stanford.
  2. Intrusion Detection (ICSI) – High-speed Layer-7 packet filtering for security.

## Slide 8: 5. Conclusion & Future Work
NetFPGA-v2
  significantly improves usability, performance, and research applications.
Future Enhancements:
  Better diagnostic tools.
  Improved drivers for multiple OS platforms.
  Exploration of embedded CPUs (PowerPC & MicroBlaze).

## Slide 9: Thanks for watching
EE533 Reading#5
Haoran Fan
USC ID: 9122-3344-95