## Slide 1: Reconfigurable Content-Based Router Using Hardware-Accelerated Language Parser
EE533 Reading#7s
Haoran Fan
USC ID: 9122-3344-95

## Slide 2: 1. Introduction
Increasing demand for fast and flexible pattern matchers in biotechnology & computer networks.
Traditional approaches sacrifice expressive power for performance.
This paper presents a scalable, high-speed regular expression matcher and a hardware-accelerated parser.
Key Innovation: Combining pattern matching with semantic parsing for content-based routing.

## Slide 3: 2. Key Contributions
High-Speed Pattern Matching
  FPGA-based regular expression matcher with a throughput of 12.90 Gbps.
  Efficient scalable logic architecture that minimizes circuit size and maximizes performance.
Hardware-Accelerated Parsing
  Direct mapping of regular grammars onto FPGA.
  Enables context-aware pattern matching.
Content-Based Routing Application
  Implemented on FPGA platform for high-speed XML message routing at 3.2 Gbps.

## Slide 4: 3. Background & Related Work
Hardware-Accelerated Pattern Matching
  Several FPGA-based designs exist:
    Nondeterministic Finite Automata (NFA) mapping (Sidhu & Prasanna, 2001).
    Deterministic Finite Automata (DFA) conversion (Moscola et al., 2003).
    Pipelined architectures for efficient hardware implementation (Baker & Prasanna, 2004).
Hardware-Accelerated Parsing
  Prior approaches used CYK algorithm but were memory-intensive.
  Recent work introduced LL(1) and LR(1) parsers in hardware, but lacked speed.

## Slide 5: 4. Proposed Pattern Matching Architecture
Timed Segment Matching (TSM)
  Combines benefits of pipelined character grid & regular expression chain.
  Key Features:
    Compact FPGA logic with minimal overhead.
    Efficient use of LUTs (Look-Up Tables) and DFFs (Flip-Flops).
    Supports scalable pattern matching at 12.90 Gbps.
Performance Comparison
  TSM vs. Other Methods:
    Faster than regex chains.
    More compact than pipelined grids.
    Efficient LUT & DFF usage enables handling large pattern sets.

## Slide 6: 5. Hardware-Accelerated Parsing
Converts regular grammars into nondeterministic finite automata (NFA)
Eliminates lookup tables, leveraging FPGA logic for high-speed parsing
Automated VHDL Generation for easy implementation

## Slide 7: 6. Content-Based Routing with XML Parsing
Objective
  Route messages based on semantic content, not just simple pattern matching.
Architecture
  Pattern Matcher – Detects XML elements.
  Parsing Structure – Extracts semantic meaning.
  Routing Module – Uses extracted info to route messages dynamically.
Implementation & Results
  Deployed on Xilinx Virtex FPGA.
  Achieves 3.2 Gbps XML routing (potential 6.4 Gbps without protocol overhead).
  Efficient resource usage (only 9% of available flip-flops).

## Slide 8: 7. Conclusion
Novel FPGA-based architecture for high-speed pattern matching & parsing.
Efficient and scalable design for content-based routing applications.
Demonstrates feasibility of semantic-based network processing at multi-gigabit speeds.

## Slide 9: Thanks for watching
EE533 Reading#7
Haoran Fan
USC ID: 9122-3344-95