## Slide 1: NetThreads: Programming NetFPGA with Threaded Software
EE533 Reading#8
Haoran Fan
USC ID: 9122-3344-95

## Slide 2: 1. Introduction
NetFPGA: A hardware platform for high-speed networking research
Challenge: Traditional hardware design for packet processing is complex and error-prone.
Solution: Use soft processors on FPGAs for flexibility and programmability.
Proposal: NetThreads – a multithreaded soft multiprocessor system for efficient packet processing

## Slide 3: 2. Why Soft Processors?
Programmable in C (simpler than hardware description languages).
  Portable across FPGA generations.
  Flexible and customizable.
  Well-suited for irregular packet-processing tasks.

## Slide 4: 3. NetThreads Architecture
Multithreading: Reduces stalls and tolerates memory/synchronization latencies.
  Memory System:
  Separate instruction, input, output, and shared memory.
  Efficient memory access with FPGA block-RAM limitations.
  Multi-Processor Support:
  Scalable design (subject to application parallelism).

## Slide 5: 4. Applications Tested
UDHCP (Dynamic Host Configuration Protocol server).
  Packet Classifier (Deep packet inspection using regex matching).
  NAT (Network Address Translation with flow tracking).

## Slide 6: 5. Key Findings
Performance Bottlenecks
  Synchronization overhead: Critical sections and lock contention reduce scalability.
  Thread scheduling optimization: Helps mitigate synchronization delays.
  Task size variance: Leads to inconsistent performance.
Throughput Observations
  Single CPU vs. Dual CPU: Minimal performance gain due to synchronization overhead.
  Packet drop tolerance: Allowing minor packet drops significantly boosts performance.

## Slide 7: 6. Experimental Results
Peak Performance:
  124k packets/sec (64B packets, single CPU)
  >58k packets/sec (1518B packets, dual CPU)
Resource Utilization:
  71% of FPGA block RAM used.
  66% of FPGA slices occupied.

## Slide 8: 7. Future Work
Custom Accelerators: Speed up execution by offloading complex tasks to specialized hardware.
Transactional Execution: Reduce synchronization bottlenecks using optimistic concurrency.

## Slide 9: 8. Future Work
NetThreads provides a programmable, parallel processing environment for NetFPGA.
Main bottleneck: Synchronization and lock contention.
Potential improvements: Hardware acceleration and optimized concurrency models.

## Slide 10: Thanks for watching
EE533 Reading#8
Haoran Fan
USC ID: 9122-3344-95